## Slide 1
ADT 101: Introduction to the Airframe Digital Twin Concept
13 Feb 2013
Eric Tuegel
AFRL/RQVS
Air Force Research Laboratory

## Slide 2: Outline
What is an ADT?
Why an ADT?
Vision of how an ADT might be used
R&D Taxonomy for the ADT
  Definitions of Taxonomy elements

## Slide 3: What is an ADT?
Physics-based Multi-scale, Multi-Discipline Models
Applied Loads & Environments
(Probabilistic)
Range of Structural Response & Reliability
(Probabilistic)
Airframe Digital Twin
Geometry & Material Data
(Probabilistic)
Plan Maintenance
Usage
State
Update
Update
Update

## Slide 4: ADT Definition
Integrated system of data, models, and analysis tools to represent an airframe over its entire life cycle …
To provide actionable information for making decisions
Now (diagnosis) and for the future (prognosis)
On a fleet-wide and individual tail number basis
Considering all sources of uncertainty

## Slide 5: Functional ADT Flowchart
Prognostics History
Health History
Failure History
Mission History
Maintenance History
Model Information
Spare Assets
Reliability Sufficient
Reliability Insufficient
Update history as new damage state and usage information is gathered
Update configuration
State of Health
Remaining Useful Life (RUL)
Rate of Change
Time to Action
Problem Identification
Components Affected
Recommendations
Confidence
Mission Readiness
Remarks/Comments
Probabilistic
Decision
Making
Structural Analysis
Notes: Damage State Awareness and Usage provides the inputs. Structural Analysis provides the prognostic model. Probabilistic Prognosis & Decisions defines the required outputs from the prognostic model. Structural Modifications result from Probabilistic Prognosis & Decisions and become inputs to the prognostic model for future analyses.

## Slide 6: Why an ADT?
Many different information streams over the life of an aircraft
Provide a singe location where all information is collected
  Able to find and use the information throughout the lifecycle
Separate information by individual aircraft
Information includes data, analysis models, etc.
  Verification and Validation of information is important

## Slide 7: Uses of the ADT (1 of 3)
Design
  Nominal ADT created as framework for individuals
  Use to assess reliability of overall design
  Manage design changes
Manufacturing & Assembly
  Collect data on individual aircraft as-built
  Create unique ADT for each tail number
  Use to disposition any discrepancies
  Configuration control of individual aircraft
“Digital Thread” Integrating across these Phases.

## Slide 8: Uses of the ADT (2 of 3)
Testing & Evaluation
  Validate or calibrate models in ADT
  Simulate conditions impossible to test
  Use to resolve anomalous test results
Use Deterministic, “Design-to” Model Now

## Slide 9: Uses of the ADT (3 of 3)
Operations
  Force structure planning
  Asset selection for mission
Maintenance, Repair & Overhaul
  Schedule and Plan Maintenance
  Capture field maintenance data
  Spares Planning
  Design Repairs
  Configuration Control of Individual Aircraft
  Problem Resolution
Several SPO’s Have Maintenance Databases

## Slide 10: ADT R&D Taxonomy
Integrated Architecture
Probabilistic Support for Decisions
Design
T&E
Manufacturing
& Assembly
Operations
Sustainment
& MRO
Computing / Computational Techniques
Data Management
Structural/Life Analysis
State Awareness
Usage

## Slide 11: Usage
External macro-conditions applied to and experienced by the aircraft as a whole
  Aerodynamic loads
  Environmental conditions (humidity, salt spray, etc.)
  Heat flux (frictional heating, exhaust impingement)
Applied to ADT as boundary conditions or forcing functions

## Slide 12: State Awareness
Knowledge of the condition of the airframe from direct observation
  Micro and macro conditions
Initial state from material & process specs, fabrication info w/ process models, design constraints, and NDI
  Initial conditions for the ADT
Operational state from NDI and documented evidence of repair or replacement
  Continuous validation of the ADT

## Slide 13: Structural & Life Analysis
Integrated collection of multi-scale, multi-discipline, multi-fidelity models of the airframe
  Quantify uncertainty probabilistically
Outputs: structural displacements, strains, and stresses; evolution of the structural, material, and damage states; and estimates future airframe condition given the proposed usage

## Slide 14: Data Management
Architecture and procedures for:
  Assuring and maintaining integrity of information
  Storing information
  Accessing desired information later
  Manipulating desired information (visualization, etc.)
Types of information:
  Usage (flight records)
  State of airframe (inspection records)
  Analysis models and results
  Maintenance records

## Slide 15: Computing
Hardware and software architectures required to efficiently execute the Structural & Life Analysis models, and access information

## Slide 16: Probabilistic Decision Support
Approaches for quantifying and managing uncertainty in the ADT
Verification & Validation of ADT
  Or possibly calibrating
Tools for making decisions from uncertain information (quantified uncertainty)
Affects:
  Model development and execution
  Data collection, archiving, and retrieval

## Slide 17: Integrated Architecture
Definition and management of the information flow between all components of the ADT, as well as between the ADT and the external world
Service-oriented, modular, open architecture
  Securely delivers the right information to the right person at the right time

## Slide 18: Design
Definition of the structural configuration
  Requirements: original and derived
  Design Allowables
  Geometry and Tolerances
  Materials Specifications
  Process Specifications
Developmental testing to support Design Allowables

## Slide 19: Manufacturing & Assembly
What is actually built and how it is built
  Actual Material Properties (ICME if possible)
  Actual dimensions of parts and assemblies
  Fit up and shimming
  Process controls and records
  Discrepancies and dispositions

## Slide 20: Test & Evaluation
Certification and Validation of the Design
  Ground Tests
  Flight Tests
  Operational Readiness Tests
Test Conditions and Results

## Slide 21: Operations
Aircraft is available and mission capable
  Environment while on the ground
  Ground handling and Payload loading
  Flight loads and environment

## Slide 22: Maintenance, Repair & Overhaul
Inspections and maintenance at any location
  Inspections and findings
    Including disassembly for access
  Repairs
  Modifications
  Program Depot Maintenance

## Slide 23: Conclusion
Still a work in progress
The ADT will have many uses – good thing